## Slide 1: Veryl: A New HDL as an Alternative to SystemVerilog
Naoya Hatta
PEZY Computing K.K.

## Slide 2: Veryl
A new HDL being developed as open-source software
  Refined syntax based on SystemVerilog
  Compile into human-readable SystemVerilog
// Counter
module Counter #(
parameter WIDTH = 1
)(
input logic i_clk ,
input logic i_rst_n,
output logic [WIDTH-1:0] o_cnt
);
logic [WIDTH-1:0] r_cnt;
always_ff @ (posedge i_clk or negedge i_rst_n) begin
if (!i_rst_n) begin
r_cnt <= 0;
end else begin
r_cnt <= r_cnt + 1;
end
end
endmodule
/// Counter
module Counter #(
param WIDTH: u32 = 1,
)(
i_clk: input clock ,
i_rst: input reset ,
o_cnt: output logic<WIDTH>,
){
var r_cnt: logic<WIDTH>;
always_ff {
if_reset {
r_cnt = 0;
} else {
r_cnt += 1;
}
}
}
SystemVerilog
Veryl
Compile

## Slide 3: Agenda
Motivation
  Enhancing SystemVerilog development
Existing approach: Alternative HDLs
  Overview and challenges
Veryl: A new HDL as an alternative to SystemVerilog
  Concept and vision
  Key features and benefits
Conclusion
  Development status

## Slide 4: Agenda
Motivation
  Enhancing SystemVerilog development
Existing approach: Alternative HDLs
  Overview and challenges
Veryl: A new HDL as an alternative to SystemVerilog
  Concept and vision
  Key features and benefits
Conclusion
  Development status

## Slide 5: Enhancing SystemVerilog Development
Possible ways
  Introduce useful SystemVerilog features
  Introduce new tools

## Slide 6: Introduce Useful SystemVerilog Features
No tool supports all features completely
  Each tool has a different support area for features
Synthesizability is not guaranteed
Introducing inexperienced features is challenging
  Need to explore usable feature combinations
System
Verilog
RTL
Simulation
Logic
Synthesis
Equivalence
Check
FPGA
Implementation
Netlist
Feature A
supported
Feature B / C
supported
Feature A / C
supported

## Slide 7: Introduce New Tools
A variety of support tools for programming languages
  e.g., linters, formatters, and specialized editors
In contrast, it is difficult to develop such support tools for SystemVerilog
  Complex syntax and semantics make it very challenging
Few options for support tools in SystemVerilog
  Very limited choice of both commercial and open-source software
System
Verilog
RTL
Simulation
Logic
Synthesis
Equivalence
Check
FPGA
Implementation
Netlist
Support
Tools

## Slide 8: Enhancing SystemVerilog Development
Possible ways
  Introduce useful SystemVerilog features
  Introduce new tools
Both approaches are difficult
How about the existing alternative HDLs?
  For example, Chisel

## Slide 9: Agenda
Motivation
  Enhancing SystemVerilog development
Existing approach: Alternative HDLs
  Overview and challenges
Veryl: A new HDL as an alternative to SystemVerilog
  Concept and vision
  Key features and benefits
Conclusion
  Development status

## Slide 10: Overview of Existing Alternative HDLs
Advantages over SystemVerilog
  Extensible language features
  Reuse the existing ecosystem

## Slide 11: Extensible Language Features
Alternative HDLs as software libraries
  For example, Chisel is developed as a library in Scala
Generate standard Verilog
  Ensuring compatibility with existing EDA tools
Flexible features integration
  New features can be added freely without compatibility issues
Verilog
RTL
Simulation
Logic
Synthesis
Equivalence
Check
FPGA
Implementation
Netlist
Compile
Chisel
Lint Check
Format
Adding
new features
Chisel
Library
No compatibility
issues

## Slide 12: Reuse the Existing Ecosystem
Based on programming language
  Compiler and tooling ecosystem can be used as is
  Sophisticated language features compared to traditional HDLs
  Software libraries can be easily integrated
Quick development can be achieved
  Both compiler and logic design
Verilog
RTL
Simulation
Logic
Synthesis
Equivalence
Check
FPGA
Implementation
Netlist
Compile
Chisel
Lint Check
Format
Scala
ecosystem
Chisel
Library
Scala
Library

## Slide 13: Overview of Existing Alternative HDLs
Advantages over SystemVerilog
  Extensible language features
  Reuse the existing ecosystem
There are some good points
Can alternative HDLs be used instead of SystemVerilog?

## Slide 14: Challenges in Using Alternative HDLs
Syntax is not optimal
Semantics differences from Verilog
Interoperability with SystemVerilog

## Slide 15: Syntax is not optimal
Take over the base language syntax
  Extensibility is limited
  HDL-specific syntax can’t be introduced
Verilog
RTL
Simulation
Logic
Synthesis
Equivalence
Check
FPGA
Implementation
Netlist
Compile
Chisel
Lint Check
Format
Scala
source code
Chisel
Library
import chisel3._
class Mux2IO extends Bundle {
val sel = Input(UInt(1.W))
val in0 = Input(UInt(1.W))
val in1 = Input(UInt(1.W))
val out = Output(UInt(1.W))
}
class Mux2 extends Module {
val io = IO(new Mux2IO)
io.out := (io.sel & io.in1) | (~io.sel & io.in0)
}
Chisel
Bit width notation
Nested function calls are required
IO is a general variable

## Slide 16: Semantics differences from Verilog
Small code generates voluminous Verilog
  Low readability of generated Verilog
  Debug with generated flat signals
Debug in Verilog side is difficult
Verilog
RTL
Simulation
Logic
Synthesis
Equivalence
Check
FPGA
Implementation
Netlist
Compile
Chisel
Lint Check
Format
Sophisticated
data structure
Voluminous
code
Chisel
Library
Debug with
flat signals

## Slide 17: Semantics differences from Verilog
Small changes in code cause large-scale changes in Verilog
  Predicting induced changes is difficult
Changing generated Verilog in detail is difficult
  Timing improvement
  pre/post-mask ECO flow
Verilog
RTL
Simulation
Logic
Synthesis
Equivalence
Check
FPGA
Implementation
Netlist
Compile
Chisel
Lint Check
Format
How should
be changed?
Logic change
is required
Chisel
Library
Timing
error

## Slide 18: Interoperability with SystemVerilog
Verilog Wrapper
SystemVerilog can’t be used directly
  A Verilog wrapper is required
Integrating into existing SystemVerilog projects is difficult
Verilog
RTL
Simulation
Logic
Synthesis
Equivalence
Check
FPGA
Implementation
Netlist
Compile
Chisel
Lint Check
Format
System
Verilog
Chisel
Library

## Slide 19: Challenges in Using Alternative HDLs
Syntax is not optimal
Semantics differences from Verilog
Interoperability with SystemVerilog
The existing alternative HDLs are difficult to use as alternatives to SystemVerilog
A new HDL is required: Veryl

## Slide 20: Agenda
Motivation
  Enhancing SystemVerilog development
Existing approach: Alternative HDLs
  Overview and challenges
Veryl: A new HDL as an alternative to SystemVerilog
  Concept and vision
  Key features and benefits
Conclusion
  Development status

## Slide 21: Introduction to Veryl Concept
Optimized syntax for synthesizable HDL
  Designed to enhance readability and reliability
Generate human-readable SystemVerilog
  Ensures generated code is easy to understand and debug
Productivity tools by default
  Incorporates tools that enhance developer productivity automatically

## Slide 22: Introduction to Veryl Concept
Optimized syntax for synthesizable HDL
  Designed to enhance readability and reliability
Generate human-readable SystemVerilog
  Ensures generated code is easy to understand and debug
Productivity tools by default
  Incorporates tools that enhance developer productivity automatically

## Slide 23: Optimized Syntax for Synthesizable HDL
Basic syntax
  Streamlined for easier understanding and use
Clock and reset
  Simplified handling of clock and reset signals
  Quickly detection of errors around clock and reset
Generics
  Enhanced support for generics to increase flexibility and reusability

## Slide 24: Basic Syntax
Comparison between SystemVerilog and Veryl
// Counter
module Counter #(
parameter WIDTH = 1
)(
input logic i_clk ,
input logic i_rst_n,
output logic [WIDTH-1:0] o_cnt
);
logic [WIDTH-1:0] r_cnt;
always_ff @ (posedge i_clk or negedge i_rst_n) begin
if (!i_rst_n) begin
r_cnt <= 0;
end else begin
r_cnt <= r_cnt + 1;
end
end
always_comb begin
o_cnt = r_cnt;
end
endmodule
/// Counter
module Counter #(
param WIDTH: u32 = 1,
)(
i_clk: input clock ,
i_rst: input reset ,
o_cnt: output logic<WIDTH>,
){
var r_cnt: logic<WIDTH>;
always_ff {
if_reset {
r_cnt = 0;
} else {
r_cnt += 1;
}
}
always_comb {
o_cnt = r_cnt;
}
}
Documentation comments
Trailing comma
SystemVerilog
Veryl
Bit width
notation
Context-aware
assignment
Simplify idiomatic syntax
in SystemVerilog
Introduce language features of
modern programming language

## Slide 25: Clock and Reset
Dedicated clock and reset type
  Sensitivity list can be omitted in single-clock modules
module Counter #(
param WIDTH: u32 = 1,
)(
i_clk: input clock ,
i_rst: input reset ,
o_cnt: output logic<WIDTH>,
){
always_ff {
if_reset {
o_cnt = 0;
} else {
o_cnt += 1;
}
}
}
Veryl
Clock and reset type
Automatically inferred clock and reset
Dedicated reset condition syntax

## Slide 26: Clock and Reset
Synchronicity and polarity configurable during compiling
  Sensitivity list and reset condition are automatically adjusted
  Single Veryl code can be compiled for both ASIC and FPGA
always_ff @ (posedge i_clk or negedge i_rst) begin
if (!i_rst) begin
end
end
always_ff @ (negedge i_clk) begin
if (i_rst) begin
end
end
module ModuleA (
i_clk: input clock,
i_rst: input reset,
) {
always_ff {
if_reset {
}
}
}
clock_type = posedge
reset_type = async_low
clock_type = negedge
reset_type = sync_high
SystemVerilog
Veryl
SystemVerilog

## Slide 27: Clock and Reset
Synchronicity and polarity configurable during compiling
  Special types indicating synchronicity and polarity are supported too
always_ff @ (posedge i_clk) begin
if (i_rst) begin
end
end
module ModuleA (
i_clk: input clock_posedge,
i_rst: input reset_sync_high,
) {
always_ff {
if_reset {
}
}
}
any clock_type
any reset_type
Veryl
SystemVerilog
Clock and reset types
indicating synchronicity and polarity

## Slide 28: Clock and Reset
Clock domain annotation
  Annotation is mandatory in multi-clock modules
  Unexplicit clock domain crossings are detected as error
module ModuleA (
i_clk_a: input `a clock,
i_dat_a: input `a logic,
o_dat_a: output `a logic,
i_clk_b: input `b clock,
o_dat_b: output `b logic,
) {
always_ff (i_clk_a) {
o_dat_a = i_dat_a;
}
unsafe (cdc) {
assign o_dat_b = i_dat_a;
}
}
Veryl
Assignment in the same clock domain is OK
Clock domain crossing
requires unsafe block
Signals belonging
clock domain `a
Signals belonging
clock domain `b
annotation

## Slide 29: Generics
Type parameter to reduce code duplication
module SramQueueVendorA;
SramVendorA u_sram();
// queue logic
}
module SramQueueVendorB;
SramVendorB u_sram();
// queue logic
}
module Test {
SramQueueVendorA u0_queue();
SramQueueVendorB u1_queue();
}
module SramQueue::<T> {
inst u_sram: T;
// queue logic
}
module Test {
// Instantiate a SramQueue by SramVendorA
inst u0_queue: SramQueue::<SramVendorA>();
// Instantiate a SramQueue by SramVendorB
inst u1_queue: SramQueue::<SramVendorB>();
}
Veryl
SystemVerilog
Parameterized
module instance
Actual module
can be specified here
Duplicated code

## Slide 30: Introduction to Veryl Concept
Optimized syntax for synthesizable HDL
  Designed to enhance readability and reliability
Generate human-readable SystemVerilog
  Ensures generated code is easy to understand and debug
Productivity tools by default
  Incorporates tools that enhance developer productivity automatically

## Slide 31: Generate Human-readable SystemVerilog
Interoperability with SystemVerilog
  Reuse the existing SystemVerilog codebase
  Introduce Veryl to the existing SystemVerilog project gradually
Debug with SystemVerilog features
  struct and interface can be used in waveform viewers
System
Verilog
RTL
Simulation
Logic
Synthesis
Equivalence
Check
FPGA
Implementation
Netlist
Compile
Veryl
Lint Check
Format
System
Verilog
Directly interface with
SystemVerilog code
Debug with
SystemVerilog types

## Slide 32: Generate Human-readable SystemVerilog
Consistent semantics with SystemVerilog
  Predictable changes in generated SystemVerilog when modifying Veryl code
Generated SystemVerilog can be finely tuned
  Timing improvement and pre/post-mask ECO flow can be applied
System
Verilog
RTL
Simulation
Logic
Synthesis
Equivalence
Check
FPGA
Implementation
Netlist
Compile
Veryl
Lint Check
Format
Fix original
code
Regenerate
Check
equivalence
Change
by hand

## Slide 33: Introduction to Veryl Concept
Optimized syntax for synthesizable HDL
  Designed to enhance readability and reliability
Generate human-readable SystemVerilog
  Ensures generated code is easy to understand and debug
Productivity tools by default
  Incorporates tools that enhance developer productivity automatically

## Slide 34: Productivity Tools by Default
Real-time diagnostics
  Editor integration using standardized language server protocol
Visual Studio Code
Vim

## Slide 35: Productivity Tools by Default
Automatic document generation
  Supports Markdown format and waveform description
/// This is a sample module.
///
/// ```wavedrom
/// {signal: [
/// {name: 'i_clk', wave: 'p......'},
/// {name: 'i_dat', wave: 'x.=x...', data: ['data']},
/// {name: 'o_dat', wave: 'x...=x.', data: ['data']},
/// ]}
/// `
pub module Sample #(
/// Data Width
param WIDTH: u32 = 1,
)(
i_clk: input clock , /// Clock
i_dat: input logic<WIDTH>, /// Input Data
o_dat: output logic<WIDTH>, /// Output Data
){}
Veryl

## Slide 36: Productivity Tools by Default
Other features
  Auto formatting for cleaner, standardized code layout
  Integrated unit testing to streamline testing process
  Ability to publish projects as libraries for easy reuse
  Dependency management for efficient handling of project dependencies

## Slide 37: Agenda
Motivation
  Enhancing SystemVerilog development
Existing approach: Alternative HDLs
  Overview and challenges
Veryl: A new HDL as an alternative to SystemVerilog
  Concept and vision
  Key features and benefits
Conclusion
  Development status

## Slide 38: Conclusion
Veryl: A new HDL as an alternative to SystemVerilog
  Optimized syntax for synthesizable HDL
  Generate human-readable SystemVerilog
  Productivity tools by default
Open-source development
  Developed as open-source software
  Available on GitHub: https://github.com/veryl-lang/veryl

## Slide 39: Development Status
Project Status
  GitHub Stars : 448
  Commits : 1778
  Issues : 54 Open, 211 Closed
  Pull Requests : 0 Open, 563 Closed
  Contributors : 9
Resources
  Official site : https://veryl-lang.org
  Language reference : https://doc.veryl-lang.org/book/
  Playground : https://doc.veryl-lang.org/playground/

## Slide 40: Questions